## Slide 1
Department of Computer Science & Engineering
Project Work Phase – II (15CSP85)
Review 2
Title: Women Security System
Guide: Swathi K
Asst. Prof, Dept of CSE
GROUP-04 BATCH-09
Team Members: 1. Sirisha M (1KS15CS102)
2. Siddharth Meharwade (1KS15CS099)
3. Suraj Kumar (1KS15CS109)
4. Shiv Shankar Sah (1KS15CS095)
Date: 03/04/19

## Slide 2: Problem Statement
In an emergency situation like being stalked, physical assault, violence, any women for that matter gets panicked hence to safe-guard herself she needs to inform about her location and status to her close ones.
When in panic, she may not be able to operate her smartphone safety applications immediately, also while using it she may be attacked.
Hence there is a need for immediate protection and alerting her close one’s, hence our security system can be adopted to overcome such situations.

## Slide 3: Objectives
The main aim of our project “Women Security System” is to provide an effective and smart way of alerting the victim’s (women in danger) close one’s about her location when she’s in danger.(This is just a Prototype).
This Project presents a women safety detection system using GPS and GSM modems.
  This detection and messaging system is composed of a GPS receiver, Microcontroller and a GSM Modem. GPS Receiver gets the location information from satellites in the form of latitude and longitude.
  A GSM modem is interfaced to the MCU. The GSM modem sends an SMS to the predefined mobile number and protect the women from danger.
We provide the system in a hidden way using a handbag.

## Slide 4: Technology Used
HARDWARE:
  Microcontroller - Arduino
  Display - 16X2 LCD
  Communication - GPS/GSM
  Sensors - heart beat sensor
  Display - 16X2 LCD
SOFTWARE:
  Embedded C with Arduino – An embedded system is combination of computer hardware and software, either fixed incapability or programmable, that is specifically designed for particular kind of application device

## Slide 5: System Design
Fig : System Block Design

## Slide 6: System Design
LCD DISPLAY-LCDs are available to display arbitrary images which can be displayed or hidden, such as pre-set words, digits and 7 segment displays as in a digital clock..
CRYSTAL OSCILLATOR: Crystal oscillator is used to produce oscillated pulses which is given to the microcontroller.

## Slide 7: System Design
GSM MODEM: Global system for mobile communication (GSM) is a globally accepted standard for digital cellular communication which
GPS RECEIVER: GPS, in full Global Positioning System, space-based radio-navigation system that broadcasts highly accurate navigation pulses to users on or near the Earth.

## Slide 8: Implementation-Software
Fig a: Opening a new project.
Fig b: Selection of board and MCU
Fig c: Selection of serial port
Fig b
Fig a
Fig c

## Slide 9: Implementation-Hardware
Arduino Microcontroller
Arduino UNO is a single-board microcontroller.
Cost less and provides a miniature computer system.
It contains everything needed to support the microcontroller Like:
  Digital and analog pin.
  16 MHz Quartz crystal.
  USB connection .

## Slide 10: Implementation-Hardware
Transformer
Rectifier
Filter
Regulator
Load /Circuit
Power Supply
AC Supply
DC Supply
POWER SUPPLY CIRCUIT
Power supply circuit convert the 220v supply to 12v power supply.
It also convert the AC power supply to DC power Supply.
Fig: Power Conversion diagram

## Slide 11: Implementation-Code
Code Snippets are added here:
#include <LiquidCrystal.h>
#include <stdio.h>
#include <SoftwareSerial.h>
SoftwareSerial mySerial(8, 9);
LiquidCrystal lcd(6, 7, 5, 4, 3, 2);
// defines pins numbers
//New GPS GY-GPS6MV2
int panic = 11;
int button = A1; //shock
int heart = 10;
int relay = 12;
Snippet : Showing Declaration of variables

## Slide 12: Implementation-Code
Code Snippets : SMS Sending
Serial.write("AT+CMGS=\"");
Serial.write(pastnumber);
Serial.write("\"\r\n"); delay(2500);
Serial.write("IOTlinks https://api.thingspeak.com/update?api_key=CYASIOD5YUQK6RJE&field1=");
converts(hbtc1);
Serial.write(0x1A); delay(4000); delay(4000);
Serial.write("AT+CMGS=\"");
Serial.write(pastnumber);
Serial.write("\"\r\n"); delay(2500);
Serial.write("IOTlinks https://api.thingspeak.com/update?api_key=CYASIOD5YUQK6RJE&field2=");
for(ii=0;ii<=6;ii++){Serial.write(finallat[ii]);}
Serial.write(0x1A); delay(4000); delay(4000);
Snippet : Showing Sending of messages.

## Slide 13: Testing And Results
Register a mobile number of the victim’s close one’s..
* followed by phone number of the person who wants to register.
We get a msg “REG” if successfully registered.
Test Successful.
Fig: Registration Step

## Slide 14: Testing And Results
After Panic Situation .
Message is sent to registered person.
Message consist of following:
  Heart Beats Rate
  GPS Location
Fig: Message After Panic to Receiver

## Slide 15: SNAPSHOTS
Fig -Power supply board with Arduino.
Fig - Panic switches

## Slide 16: SNAPSHOTS
Fig - GPS
Fig - GSM

## Slide 17: Snapshots
Fig : Showing Heart Beat and Location data using a third party app to track the victim, called thingview.

## Slide 18: Github And BlogSpot Link
https://github.com/projectwork09/Women-Security
womensecurityproject09.wordpress.com

## Slide 19: References
[1] A mobile-based women safety application (I safe Apps). Dr. Sridhar Mandapati, Sravya Pamidi, Sriharitha Ambati," A Mobile-based Women Safety Application (I Safe App)". Vol 17, Issue 1, Ver. I (Jan – Feb. 2015)
[2] Advanced Security system for women. Deepak Sharma, Abhijit Paradkar “All in one Intelligent Safety System for Women Security”. Vol 130 No.11 November 2015.
[3] Smart Shield for Women Safety. Rachana B Pawar, Manali H. Kulabkar, Kirti S. Pawar Akshata R. Tambe Prof. Smita Khairnar. “Smart Shield for Women Safety”. Volume: 05 Issue: 04 | Apr-2018

## Slide 20
Thank You